|  | ECC PT1(18)248 |
| --- | --- |
| ECC PT1 #60 |
| Dublin, Ireland, 17-21 September 2018 |
| Date issued: | 12 September 2018 |
| Source: | Lithuania |
| Subject: | L-band x-border MFCN vs. ATS |
| N Group membership required to read? (Y/N) |
| Summary: |
| Further analysis on possible interference from MFCN into telemetry system were performed. The revisions to the working document (ECC PT1(18)186 Annex 28) are provided in the Attachment. This includes: moving section on the approach how to calculate the interfering power flux density to the Annex adding new Annex for calculation of averaged value of iRSS for surrounding network including results for the elevation of -2 degrees for AP of M.1851 in Table 7 and Table 8 creating new Annex to analyse MFCN system parameters (network layout, base station antenna height and antenna downtilt) and propagation model influence into interference level updating Annex on antennas adding additional calculations for Kaliningrad case (it is proposed to move Section 7.2 to separate Annex after consideration of updated material) creating new Section regarding interference to on-board receiver |
| Proposal: |
| Update draft report accordingly. |
| Background: |
| ECC#45 has approved the WI to develop guidance for cross-border coordination between the MFCN and aeronautical telemetry systems in countries listed in No 5.342. ECC PT1 is developing the working document on this matter. |